## Slide 1
Dr. Sajid Iqbal
Department of Computer Science
Bahauddin Zakariya University, Multan

## Slide 2: Computer Hardware
Introduction to computers

## Slide 3: Motherboard
A mother board is printed circuit board
It allows other computer ICs to communicate
Mother boards are air cooled with heat sinks
It has many other sub-systems
  Central processor
  Input/output chipsets
  Memory controllers
  Interface connectors
A number of add-on cards can be installed
  Memory cards
  Processor
  Video Cards
  Sound Cards
  Network Cards
  Hard drives
  USB Controllers
  System Clock chip

## Slide 4: Motherboard
Thanks to YouTube video provider

## Slide 5: Ports
A port is an interface between motherboard and other devices
There are number of ports in mother board
Each port need specific connector

## Slide 6: Buses (Electrical Buses)
A bus is a communication system that allows communication among different computer components
Early computer buses were parallel electrical wires with multiple hardware connections
Two ways of data transfer on buses
  Parallel
  Bit-serial
Buses could be either
  Internal (local buses)
  external

## Slide 7: Electrical Buses
Bus Categories: There are three main bus categories
  Data Bus: These buses actually transfer the data from one point to another
  Address Bus: This bus specifies where data should be sent i.e. to which memory location of RAM
  Control Bus: This type of bus controls the communication i.e. when to start sending data
  Power bus: This bus supplies the current to all circuit. If no current is provided, the communication is not possible.
Bus width: The number of wires used in a bus i.e. 16, 24, 32

## Slide 8: Bus Terminology
System Bus: The bus that connects the CPU to RAM on mother board
IO Buses: Connects various peripheral devices to CPU
Expansion buses:
    ISA - Industry Standard Architecture
    EISA - Extended Industry Standard Architecture
    MCA - Micro Channel Architecture
    VESA - Video Electronics Standards Association
    PCI - Peripheral Component Interconnect
    PCI Express (PCI-X)
    PCMCIA - Personal Computer Memory Card Industry Association (Also called PC bus)
    AGP - Accelerated Graphics Port
    SCSI - Small Computer Systems Interface
    Universal Serial Bus (USB)

## Slide 9: How Buses Work
Thanks to YouTube video provider

## Slide 10: CPU Casing
There are variety of casing. You may choose one of your choice
CPU casing has space and configuration to install different computer components
Front end ports and back end ports

## Slide 11: Main Power Supply
A power supply unit (PSU) converts mains AC to low-voltage regulated DC power for the internal components of a computer
Modern personal computers universally use switched-mode power supplies
Some power supplies have a manual switch for selecting input voltage, while others automatically adapt to the mains voltage

## Slide 12
Thanks for watching
Dr. Sajid Iqbal
Assistant Professor
Department of Computer Science
Bahauddin Zakariya University, Multan
sajidiqbal.pk@gmail.com
https://github.com/sajjo79/Introduction-to-Computers
Allah Hafiz
COMEDXD